Inspection Date:

Prepared For:

Prepared By:

Get The Facts Home Inspection

P.O. Box 6118

Brandon, Fl. 33508

813-785-4620

Fax

Joe@GetTheFactsHomeINspection.com

Report Number:

Inspector:

© 2011 Get The Facts Home Inspection

# TABLE OF CONTENTS

Report Overview	3

Receipt/Invoice	4

Grounds	5

Roof	6

Exterior	7

Garage	9

Kitchen	10

Laundry	11

Bathrooms	12

Rooms	14

Interior	16

Basement	17

Crawl	18

Plumbing	19

Heating	20

Electric/Cooling	21

Summary	22

# Report Overview

## THE HOUSE IN PERSPECTIVE

## CONVENTIONS USED IN THIS REPORT

SATISFACTORY - Indicates the component is functionally consistent with its original purpose but may show signs of normal wear and tear and deterioration.

MARGINAL - Indicates the component will probably require repair or replacement anytime within five years.

POOR - Indicates the component will need repair or replacement now or in the very near future.

MAJOR CONCERNS - A system or component that is considered significantly deficient or is unsafe.

SAFETY HAZARD - Denotes a condition that is unsafe and in need of prompt attention.

## THE SCOPE OF THE INSPECTION

All components designated for inspection in the ASHI( Standards of Practice are inspected, except as may be noted in the “Limitations of Inspection” sections within this report.

It is the goal of the inspection to put a home buyer in a better position to make a buying decision.  Not all improvements will be identified during this inspection.  Unexpected repairs should still be anticipated.  The inspection should not be considered a guarantee or warranty of any kind.

Please refer to the pre-inspection contract for a full explanation of the scope of the inspection.

## Building Data

Approximate Age:

Style:

Main Entrance Faces:

State of Occupancy:

Weather Conditions:

Recent Rain:

Ground cover:

# RECEIPT / INVOICE

Get The Facts Home Inspection

P.O. Box 6118

Brandon, Fl. 33508

813-785-4620

Date: 	Inspection Number:

Name:

| Inspection: |  |
| --- | --- |
| Other** |  |
| Total: |  |

Check #:

Cash

Credit Card:

**	 Radon	 Pool / Hot Tub	 Shipping	 Well & Septic	 WDO/WDI

Inspected By:

License/Certification #:

| Service Walks | None Not visible Public sidewalk needs repair |
| --- | --- |

Material:	 Concrete	 Flagstone	 Gravel 	 Brick

Condition:	 Satisfactory	 Marginal	 Poor	 Trip Hazard	 Typical cracks

Pitched towards home (See remarks)	 Settling cracks

| Driveway/parking | None Not visible |
| --- | --- |

Material:	 Concrete	 Asphalt	 Gravel/Dirt 	 Brick

Condition:	 Satisfactory	 Marginal	 Poor	 Settling Cracks	  Typical cracks

Pitched towards home (See remarks)	 Trip hazard	  Fill cracks and seal

| Porch (covered entrance) | None Not visible |
| --- | --- |

Support Pier:	 Concrete	 Wood

Condition:	 Satisfactory	 Marginal	 Poor	 Railing/Balusters recommended

Floor:	 Satisfactory	 Marginal	 Poor	 Safety Hazard

| Stoops/Steps | None one Uneven risers Rotted/Damaged Cracked Settled |
| --- | --- |

Material:	 Concrete	 Wood		       Railing/Balusters recommended

Condition: 	 Satisfactory	 Marginal	 Poor	       Safety Hazard

| Patio | None |
| --- | --- |

Material:	 Concrete 	 Flagstone	 Kool-Deck®	 Brick

Condition:	 Satisfactory	 Marginal	 Poor	 Settling Cracks	 Trip hazard

Pitched towards home (See remarks)	 Drainage provided	 Typical cracks

| Deck/Balcony (flat, floored, roofless area) | None Not visible |
| --- | --- |

Material:	 Wood		 Metal	 Composite	 Railing/Balusters recommended

Finish:	 Treated                Painted/Stained

Safety Hazard	 Improper attachment to house 	 Railing loose

Condition:	 Satisfactory	 Marginal	 Poor	 Wood in contact with soil

| Deck/Patio/Porch Covers | None Earth to wood contact Moisture/Insect damage |
| --- | --- |

Condition:	 Satisfactory	 Marginal	 Poor	 Posts/Supports need Repair

Recommend:	 Metal Straps/Bolts/Nails/Flashing	 Improper attachment to house

| Fence/Wall | Not evaluated None |
| --- | --- |

Type:	 Brick/Block	 Wood	 Metal	 Chain Link	 Rusted		 Vinyl

Condition:	 Satisfactory	 Marginal	 Poor	 Typical cracks 	 Loose Blocks/Caps

Gate:	 N/A	 Satisfactory	 Marginal	 Poor	 Planks missing/damaged

| Landscaping Affecting Foundation | (See remarks) |
| --- | --- |

Negative Grade:	 East		 West	 North	 South	 Satisfactory

Recommend additional backfill	 Recommend window wells/covers	 Trim back trees/shrubberies

Wood in contact with/improper clearance to soil

| Retaining Wall | None Material: Drainage holes recommended |
| --- | --- |

Condition:	 Satisfactory	 Marginal	 Poor	 Safety Hazard	 Leaning/cracked/bowed

(Relates to the visual condition of the wall)

| Hose Bibs | None No anti-siphon valve Recommend Anti-siphon valve |
| --- | --- |

Operable:	 Yes	 No	 Not tested	 Not on

| General Comments |  |
| --- | --- |

| Roof Visibility | All Partial None Limited by: |
| --- | --- |

| Inspected From | Roof Ladder at eaves Ground (Inspection Limited) With Binoculars |
| --- | --- |

| Style of Roof |  |
| --- | --- |

Type:	 Gable	 Hip	 Mansard	 Shed	 Flat

Pitch:	 Low	 Medium    	 Steep	 Flat

Roof #1	Type: 	Layers: 	Approx. ageYrs.
Roof #2	Type: 	Layers: 	Approx. ageYrs.
Roof #3	Type: 	Layers: 	Approx. ageYrs.

| Ventilation System | Type: Soffit Ridge Gable Roof Turbine Powered |
| --- | --- |

Ventilation Present:  Yes   No

(See Interior remarks)

| Flashing | Material: Not visible Galv/Alum Asphalt |
| --- | --- |

Copper	 Foam	 Rubber	 Lead

Condition:	 Not visible	 Satisfactory	 Marginal	 Poor	 Rusted   Missing

Separated from chimney/roof     Recommend Sealing

| Valleys | N/A Material: Not Visible Galv/Alum Asphalt Lead |
| --- | --- |

Copper

Condition:	 Not visible	 Satisfactory	 Marginal	 Poor

Holes	 Rusted	 Recommend Sealing

| Condition of Roof Coverings | Roof #1: Satisfactory Marginal Poor |
| --- | --- |
|  | Roof #2: Satisfactory Marginal Poor |
|  | Roof #3: Satisfactory Marginal Poor |

Condition:	 Curling	 Cracking	 Ponding	 Burn Spots 	 Broken/Loose Tiles/Shingles

Nail popping	 Granules missing	 Alligatoring	 Blistering	 Missing Tabs/Shingles/Tiles

Moss buildup	 Exposed felt 	 Cupping	 Incomplete/Improper Nailing
                              Recommend roofer evaluate           Evidence of Leakage

| Skylights | N/A Not visible Cracked/Broken |
| --- | --- |

Condition:		 Satisfactory	 Marginal		 Poor

| Plumbing Vents | Not Visible Yes No Satisfactory Marginal Poor |
| --- | --- |

Conditions reported above reflect visible portion only. See additional Comments

| General Comments |  |
| --- | --- |

| Chimney(s) | None Location(s): |
| --- | --- |

Viewed From:	 Roof	 Ladder at eaves	 Ground (Inspection Limited) 	 With Binoculars

Rain Cap/Spark Arrestor:	 Yes	 No	 Recommended

Chase:	 Brick	 Stone	 Metal	 Blocks 	 Framed

Evidence of: 	 Holes in metal	 Cracked chimney cap	 Loose mortar joints	 Flaking	 Loose Brick	 Rust

Flue:	 Tile	 Metal	 Unlined	 Not visible

Evidence of: 	 Scaling	 Cracks	 Creosote	 Not evaluated (See remarks page)

Have flue(s) cleaned and re-evaluated	 Recommend Cricket/Saddle/Flashing

Condition:	 Satisfactory	 Marginal	 Poor                     	 Recommend Repair

| Gutters/Scuppers/EaveStrough | None Needs to be cleaned Downspouts needed |
| --- | --- |

Material:	 Copper	 Vinyl/Plastic	 Galvanized/Aluminum

Condition:	 Satisfactory	 Marginal	 Poor	 Rusting

Leaking:	 Corners	 Joints	 Hole in main run

Attachment:	 Loose	 Missing spikes	 Improperly sloped   (See remark)

Extension needed:	 North	 South	 East     West    Recommend repair/replacement of damaged sections

| Siding | (*See remarks page) |
| --- | --- |

Material:	 Stone	 Slate	 Block/Brick	 Fiberboard	 Fiber-cement	 Stucco

EIFS* Not Inspected	 Asphalt	 Wood	 Metal/Vinyl

Typical cracks	 Peeling paint 	 Monitor	 Wood rot	 Loose/Missing/Holes

Condition:	 Satisfactory	 Marginal	 Poor	 Recommend repair/painting

| 1.)Trim 2.)Soffit 3.)Fascia 4.)Flashing |  |
| --- | --- |

Material:	 Wood	 Fiberboard	 Aluminum/Steel	 Vinyl	 Stucco

Recommend repair/painting	 Damaged wood

Condition:	 Satisfactory	 Marginal	 Poor

| Caulking |  |
| --- | --- |

Condition:	 Satisfactory	 Marginal	 Poor

Recommend around windows/doors/masonry ledges/corners/utility penetrations

| Windows & Screens | Failed/fogged insulated glass |
| --- | --- |

Material:	 Wood	 Metal	 Vinyl	 Aluminum/Vinyl Clad

Screens:	 Torn	 Bent	 Not installed	 Glazing Compound/Caulk needed

Condition:	 Satisfactory	 Marginal	 Poor	 Wood rot	 Recommend repair/painting

| Storms Windows | None Not installed Wood Clad comb. Wood/metal comb. Metal |
| --- | --- |

Putty:	 Satisfactory	 Needed	 N/A

Condition:	 Satisfactory	 Broken/cracked	 Wood rot	 Recommend repair/painting

| Slab-on-Grade/Foundation |  |
| --- | --- |

Foundation Wall: 	 Concrete block	 Poured concrete	 Not visible

Condition:	 Satisfactory	 Marginal	 Monitor                 Have Evaluated

Concrete Slab:	 Satisfactory	 Marginal	 Monitor                 Have Evaluated

Condition reported above reflect visible portion only.

| General Comments |  |
| --- | --- |

| Service Entry | Underground Overhead Weather head/mast needs repair |
| --- | --- |

Exterior receptacles:	 Yes	 No

Operable:	 Yes	 No                 Overhead wires too low

GFCI present:	 Yes	 No	Operable:	 Yes	 No		 Safety Hazard

Reverse polarity	 Open ground(s)	   Recommend GFCI Receptacles
Condition:	 Satisfactory	 Marginal	 Poor

| Building(s) Exterior Wall Construction |  |
| --- | --- |

Type:	 Not visible	 Framed	 Masonry

Condition:	 Not visible 	 Satisfactory	 Marginal	 Poor

| Exterior Doors | 1.) ENTRANCE 2.) PATIO 3.)STORM |
| --- | --- |

Weatherstripping:	 Satisfactory	 Marginal	 Poor	 Missing	 Replace

Door Condition:	 Satisfactory	 Marginal	 Poor

| Exterior A/C - Heat Pump |  |
| --- | --- |

UNIT #1: 	 N/A	Location:

Brand: 		Model #: 	Approximate age:  yrs.

Outside Disconnect:	 Yes	 No	Maximum fuse/breaker rating: ??? Amp	Fuses/breakers installed: ??? Amp

Level:	 Yes	 No	 Cabinet/housing rusted	 Improperly sized fuses/breakers

Condenser Fins:	 Damaged	 Need cleaning	 Damaged base/pad

Damaged Refrigerant Line	Insulation:  Yes	 No     Replace

Condition:	 Satisfactory         Marginal	 Poor                        Improper Clearance (air flow)  Yes	 No

| Exterior A/C - Heat Pump |  |
| --- | --- |

UNIT #2: 	 N/A	Location:

Brand: 		Model #: 	Approximate age:  yrs.

Outside Disconnect:	 Yes	 No	Maximum fuse/breaker rating: ??? Amp	Fuses/breakers installed: ??? Amp

Level:	 Yes	 No	 Cabinet/housing rusted	 Improperly sized fuses/breakers

Condenser Fins:	 Damaged	 Need cleaning	 Damaged base/pad

Damaged Refrigerant Line	Insulation:  Yes	 No     Replace

Condition:	 Satisfactory         Marginal	 Poor                        Improper Clearance (air flow)  Yes	 No

| General Comments |  |
| --- | --- |

| Type | None |
| --- | --- |

Attached	 Detached	 1-car	 2-car	 3-car	 4-car

| Automatic Opener | Yes No Operable Inoperable |
| --- | --- |

| Safety Reverse | Operable: Yes No Need(s) adjusting Safety hazard |
| --- | --- |

| Roofing | Material: Same as house Type: Approx. Age: Approx. layers: |
| --- | --- |

| Gutters / Eavestrough | Condition: Satisfactory Marginal Poor Same as House |
| --- | --- |

| SIDING / TRIM |  |
| --- | --- |

Siding:	 Same as house	 Wood	 Metal	 Vinyl

Stucco	 Masonry	 Slate	 Fiberboard

Trim:	 Same as house	 Wood	 Aluminum	 Vinyl

| Floor |  |
| --- | --- |

Material:	 Concrete	 Gravel	 Asphalt	 Dirt

Condition:	 Satisfactory	 Typical cracks	 Large settling cracks	 Recommend evaluation/repair

Burners less than 18” above garage floor: 	 N/A	 Yes	 No	 Safety hazard

| Sill Plates | Not visible Floor level Elevated Rotted/Damaged Recommend repair |
| --- | --- |

| Overhead Door(s) | N/A |
| --- | --- |

Material:	 Wood	 Fiberglass	 Masonite	 Metal	 Recommend repair

Condition:	 Satisfactory	 Marginal	 Poor	 Overhead door hardware loose

Recommend Priming/Painting Inside & Edges:   Yes	 No	 Safety Cable Recommended     Weatherstripping missing/damaged

| Exterior Service Door | None |
| --- | --- |

Condition:	 Satisfactory	 Marginal	 Poor	 Damaged/Rusted

| Electrical recepticals Present | Yes No Not visible |
| --- | --- |

Reverse polarity:	 Yes	 No	Open ground:	 Yes	 No  	 Safety hazard

GFCI Present:	 Yes	 No	Operable:	 Yes	 No	 Handyman/extension cord wiring

Recommend GFCI Receptacles

| Fire Separation Walls & Ceiling | (Between garage & living area) |
| --- | --- |

N/A	 Present	           	 Missing

Condition:	 Satisfactory	 Recommend repair	 Holes walls/ceiling      Safety hazard(s)

Moisture Stains Present:	 Yes	 No      Typical Cracks:	 Yes		 No
Fire door:	 Not verifiable      Not a fire door  	 Needs repair	 Satisfactory
Auto closure:      N/A	 Satisfactory       Inoperative         	 Missing

| General Comments |  |
| --- | --- |

| Countertops | Satisfactory Marginal Recommend repair/caulking |
| --- | --- |

| Cabinets | Satisfactory Marginal Recommend repair/adjustment |
| --- | --- |

| Plumbing Comments |  |
| --- | --- |

Faucet Leaks:	 Yes	 No	Pipes leak/corroded:	 Yes	 No

Sink/Faucet:	 Satisfactory	 Corroded	 Chipped	 Cracked	 Recommend repair

Functional Drainage:	 Satisfactory	 Marginal	   Poor  Functional Flow:  Satisfactory    Marginal    Poor
Comments:

| Walls & Ceiling |  |
| --- | --- |

Condition:	 Satisfactory	 Marginal	 Poor	 Typical cracks	 Moisture stains

| Heating / Cooling Source | Yes No |
| --- | --- |

| Floor | Condition: Satisfactory Marginal Poor Sloping Squeaks |
| --- | --- |

Comments:

| Appliances | (See remarks page) |
| --- | --- |

Disposal	Operable:	 Yes	 No	 Trash compactor 	Operable:	 Yes	 No

Oven	Operable:	 Yes	 No	 Exhaust fan	Operable:	 Yes	 No

Range	Operable:	 Yes	 No	 Refrigerator	Operable:	 Yes	 No

Dishwasher	Operable:	 Yes	 No	 Microwave	Operable:	 Yes	 No

___________	Operable:	 Yes	 No		Operable:	 Yes	 No

Dishwasher Airgap:	 Yes	 No and/or  Dishwasher Drain Line Looped:   Yes	   No

Receptacles Present:	 Yes	 No	Operable:	 Yes	 No

GFCI:	 Yes	 No	Operable:	 Yes	 No   Recommend GFCI Receptacles

Open ground/Reverse polarity:	 Yes     No     Potential safety hazard(s)

| General Comments |  |
| --- | --- |

| Laundry |  |
| --- | --- |

Laundry sink:	 N/A	Faucet leaks:	 Yes	 No	Pipes leak:	 Yes	 No

Cross connections:	 Yes	 No	Heat source present:	 Yes	 No	Room vented:	 Yes	 No

Dryer vented:	 N/A	 Wall	 Ceiling	 Floor	 Not vented

Plastic Dryer Vent not recommended   Not vented to Exterior	 Recommend repair	 Safety hazard

Electrical: 	Open ground/reverse polarity within 6’ of water:	 Yes	 No	 Safety hazard

GFCI present:	 Yes	 No	Operable:	 Yes  	 No          Recommend GFCI Receptacles

Appliances:	 Washer	 Dryer	 Water heater	 Furnace/Boiler

Washer hook-up lines/valves:	 Leaking	 Corroded	 Not visible

Gas Shut-off Valve: 	 N/A 	 Yes	 No	 Cap Needed	 Safety hazard	 Not visible

| General Comments |  |
| --- | --- |

| Bath |  |
| --- | --- |

Sinks:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes	      No

Tubs:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes       No	 N/A

Showers:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes       No	 N/A

Toilet:	Bowl Loose:	 Yes	 No	Operable:     Yes      No     Cracked bowl    Toilet leaks

Whirlpool:	 Yes	 No     Operable:     Yes      No      Not tested     No access door

Shower/Tub area:    Ceramic/Plastic      Fiberglass      Masonite

Condition:      Satisfactory      Marginal      Poor      Rotted floors

Caulk/Grouting Needed:      Yes      No     Where:

Drainage:	 Satisfactory      Marginal      Poor

Water flow:	 Satisfactory      Marginal      Poor

Moisture stains present:	 Yes	 No      Walls   Ceilings      Cabinetsy

Window/doors:	 Satisfactory      Marginal     	 Poor

Receptacles Present:	 Yes	 No	Operable:    	 Yes      No

GFCI: 	 Yes	 No	Operable:    	 Yes      No

Open ground/Reverse polarity:   	 Yes	 No	 Potential Safety Hazard(s)   (See remarks)

Heat source present:	 Yes	 No

Exhaust fan:		 Yes	 No	Operable:  Yes     No     Noisy

| General Comments | See additional comments |
| --- | --- |

| Bath |  |
| --- | --- |

Sinks:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes	      No

Tubs:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes       No	 N/A

Showers:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes       No	 N/A

Toilet:	Bowl loose:	 Yes	 No	Operable:     Yes       No     Cracked bowl    Toilet leaks

Whirlpool:	 Yes	 No     Operable:     Yes      No      Not tested     No access door

Shower/Tub area:    Ceramic/Plastic      Fiberglass      Masonite

Condition:      Satisfactory      Marginal      Poor      Rotted floors

Caulk/Grouting Needed:      Yes      No     Where:

Drainage:	 Satisfactory      Marginal      Poor

Water flow:	 Satisfactory      Marginal      Poor

Moisture stains present:	 Yes	 No      Walls   Ceilings      Cabinets

Window/doors:	 Satisfactory      Marginal	 Poor

Receptacles Present:	 Yes	 No	Operable:		 Yes      No

GFCI: 	 Yes	 No	Operable:	 Yes      No

Open ground/Reverse polarity:	 Yes	 No	 Potential Safety Hazard(s)   (See remarks)

Heat source present:	 Yes	 No

Exhaust fan:		 Yes	 No	Operable:  Yes     No     Noisy

| General Comments | See additional comments |
| --- | --- |

| Bath |  |
| --- | --- |

Sinks:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes	      No

Tubs:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes       No	 N/A

Showers:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes       No	 N/A

Toilet:	Bowl Loose:	 Yes	 No	Operable:     Yes      No     Cracked bowl    Toilet leaks

Whirlpool:	 Yes	 No     Operable:     Yes      No      Not tested     No access door

Shower/Tub area:    Ceramic/Plastic      Fiberglass      Masonite

Condition:      Satisfactory      Marginal      Poor      Rotted floors

Caulk/Grouting Needed:      Yes      No     Where:

Drainage:	 Satisfactory      Marginal      Poor

Water flow:	 Satisfactory      Marginal      Poor

Moisture stains present:	 Yes	 No      Walls   Ceilings      Cabinetsy

Window/doors:	 Satisfactory      Marginal     	 Poor

Receptacles Present:	 Yes	 No	Operable:    	 Yes      No

GFCI: 	 Yes	 No	Operable:    	 Yes      No

Open ground/Reverse polarity:   	 Yes	 No	 Potential Safety Hazard(s)   (See remarks)

Heat source present:	 Yes	 No

Exhaust fan:		 Yes	 No	Operable:  Yes     No     Noisy

| General Comments | See additional comments |
| --- | --- |

| Bath |  |
| --- | --- |

Sinks:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes	      No

Tubs:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes       No	 N/A

Showers:	Faucet leaks:	 Yes	 No	Pipes leak:   Yes       No	 N/A

Toilet:	Bowl loose:	 Yes	 No	Operable:     Yes       No     Cracked bowl    Toilet leaks

Whirlpool:	 Yes	 No     Operable:     Yes      No      Not tested     No access door

Shower/Tub area:    Ceramic/Plastic      Fiberglass      Masonite

Condition:      Satisfactory      Marginal      Poor      Rotted floors

Caulk/Grouting Needed:      Yes      No     Where:

Drainage:	 Satisfactory      Marginal      Poor

Water flow:	 Satisfactory      Marginal      Poor

Moisture stains present:	 Yes	 No      Walls   Ceilings      Cabinets

Window/doors:	 Satisfactory      Marginal	 Poor

Receptacles Present:	 Yes	 No	Operable:		 Yes      No

GFCI: 	 Yes	 No	Operable:	 Yes      No

Open ground/Reverse polarity:	 Yes	 No	 Potential Safety Hazard(s)   (See remarks)

Heat source present:	 Yes	 No

Exhaust fan:		 Yes	 No	Operable:  Yes     No     Noisy

| General Comments | See additional comments |
| --- | --- |

| Location: |  | UNIT # |  |
| --- | --- | --- | --- |

Walls & Ceiling:	 Satisfactory	 Marginal	 Poor	 Typical cracks	 Damage

Moisture stains:	 Yes	 No             Where:

Floor:	 Satisfactory	 Marginal	 Poor            Squeaks	 Slopes

Ceiling Fan:	 N/A 	 Satisfactory	 Marginal	 Poor

Electrical: 	Switches:	 Yes	 No	Receptacles:	 Yes	 No    Operable:	 Yes	 No

Open ground/Reverse polarity: 	 Yes	 No	 Safety Hazard 	 Cover plates missing

Heating Source Present:	 Yes	 Not visible	Holes:	 Doors	 Walls		 Ceilings

Egress Restricted:	 N/A	 Yes	 No

- Doors & Windows:      	 Satisfactory	 Marginal	 Poor	 Cracked glass

Evidence of leaking insulated glass	 Broken/Missing hardware

| Location: |  | UNIT # |  |
| --- | --- | --- | --- |

Walls & Ceiling:	 Satisfactory	 Marginal	 Poor	 Typical cracks	 Damage

Moisture stains:	 Yes	 No             Where:

Floor:	 Satisfactory	 Marginal	 Poor            Squeaks	 Slopes

Ceiling Fan:	 N/A 	 Satisfactory	 Marginal	 Poor

Electrical: 	Switches:	 Yes	 No	Receptacles:	 Yes	 No    Operable:	 Yes	 No

Open ground/Reverse polarity:	 Yes	 No	 Safety Hazard 	 Cover plates missing

Heating Source Present:	 Yes	 Not visible	Holes:	 Doors	 Walls		 Ceilings

Egress Restricted:	 N/A	 Yes	 No

- Doors & Windows:      	 Satisfactory	 Marginal	 Poor	 Cracked glass

Evidence of leaking insulated glass	 Broken/Missing hardware

| Location: |  | UNIT # |  |
| --- | --- | --- | --- |

Walls & Ceiling:	 Satisfactory	 Marginal	 Poor	 Typical cracks	 Damage

Moisture stains:	 Yes	 No             Where:

Floor:	 Satisfactory	 Marginal	 Poor            Squeaks	 Slopes

Ceiling Fan:	 N/A 	 Satisfactory	 Marginal	 Poor

Electrical: 	Switches:	 Yes	 No	Receptacles:  Yes	 No    Operable:	 Yes	 No

Open ground/Reverse polarity:	 Yes	 No	 Safety Hazard 	 Cover plates missing

Heating Source Present:	 Yes	 Not visible	Holes:	 Doors	 Walls		 Ceilings

Egress Restricted:	 N/A	 Yes	 No

- Doors & Windows:      	 Satisfactory	 Marginal	 Poor	 Cracked glass

Evidence of leaking insulated glass	 Broken/Missing hardware

| Location: |  | UNIT # |  |
| --- | --- | --- | --- |

Walls & Ceiling:	 Satisfactory	 Marginal	 Poor	 Typical cracks	 Damage

Moisture stains:	 Yes	 No             Where:

Floor:	 Satisfactory	 Marginal	 Poor            Squeaks	 Slopes

Ceiling Fan:	 N/A 	 Satisfactory	 Marginal	 Poor

Electrical: 	Switches:	 Yes	 No	Receptacles:  Yes	 No    Operable:	 Yes	 No

Open ground/Reverse polarity:	 Yes	 No	 Safety Hazard 	 Cover plates missing

Heating Source Present:	 Yes	 Not visible	Holes:	 Doors	 Walls		 Ceilings

Egress Restricted:	 N/A	 Yes	 No

- Doors & Windows:      	 Satisfactory	 Marginal	 Poor	 Cracked glass

Evidence of leaking insulated glass	 Broken/Missing hardware

| General Comments | See additional comments |
| --- | --- |

| Location: |  | UNIT # |  |
| --- | --- | --- | --- |

Walls & Ceiling:	 Satisfactory	 Marginal	 Poor	 Typical cracks	 Damage

Moisture stains:	 Yes	 No             Where:

Floor:	 Satisfactory	 Marginal	 Poor            Squeaks	 Slopes

Ceiling Fan:	 N/A 	 Satisfactory	 Marginal	 Poor

Electrical: 	Switches:	 Yes	 No	Receptacles:	 Yes	 No    Operable:	 Yes	 No

Open ground/Reverse polarity: 	 Yes	 No	 Safety Hazard 	 Cover plates missing

Heating Source Present:	 Yes	 Not visible	Holes:	 Doors	 Walls		 Ceilings

Egress Restricted:	 N/A	 Yes	 No

- Doors & Windows:      	 Satisfactory	 Marginal	 Poor	 Cracked glass

Evidence of leaking insulated glass	 Broken/Missing hardware

| Location: |  | UNIT # |  |
| --- | --- | --- | --- |

Walls & Ceiling:	 Satisfactory	 Marginal	 Poor	 Typical cracks	 Damage

Moisture stains:	 Yes	 No             Where:

Floor:	 Satisfactory	 Marginal	 Poor            Squeaks	 Slopes

Ceiling Fan:	 N/A 	 Satisfactory	 Marginal	 Poor

Electrical: 	Switches:	 Yes	 No	Receptacles:	 Yes	 No    Operable:	 Yes	 No

Open ground/Reverse polarity:	 Yes	 No	 Safety Hazard 	 Cover plates missing

Heating Source Present:	 Yes	 Not visible	Holes:	 Doors	 Walls		 Ceilings

Egress Restricted:	 N/A	 Yes	 No

- Doors & Windows:      	 Satisfactory	 Marginal	 Poor	 Cracked glass

Evidence of leaking insulated glass	 Broken/Missing hardware

| Location: |  | UNIT # |  |
| --- | --- | --- | --- |

Walls & Ceiling:	 Satisfactory	 Marginal	 Poor	 Typical cracks	 Damage

Moisture stains:	 Yes	 No             Where:

Floor:	 Satisfactory	 Marginal	 Poor            Squeaks	 Slopes

Ceiling Fan:	 N/A 	 Satisfactory	 Marginal	 Poor

Electrical: 	Switches:	 Yes	 No	Receptacles:  Yes	 No    Operable:	 Yes	 No

Open ground/Reverse polarity:	 Yes	 No	 Safety Hazard 	 Cover plates missing

Heating Source Present:	 Yes	 Not visible	Holes:	 Doors	 Walls		 Ceilings

Egress Restricted:	 N/A	 Yes	 No

- Doors & Windows:      	 Satisfactory	 Marginal	 Poor	 Cracked glass

Evidence of leaking insulated glass	 Broken/Missing hardware

| Location: |  | UNIT # |  |
| --- | --- | --- | --- |

Walls & Ceiling:	 Satisfactory	 Marginal	 Poor	 Typical cracks	 Damage

Moisture stains:	 Yes	 No             Where:

Floor:	 Satisfactory	 Marginal	 Poor            Squeaks	 Slopes

Ceiling Fan:	 N/A 	 Satisfactory	 Marginal	 Poor

Electrical: 	Switches:	 Yes	 No	Receptacles:  Yes	 No    Operable:	 Yes	 No

Open ground/Reverse polarity:	 Yes	 No	 Safety Hazard 	 Cover plates missing

Heating Source Present:	 Yes	 Not visible	Holes:	 Doors	 Walls		 Ceilings

Egress Restricted:	 N/A	 Yes	 No

- Doors & Windows:      	 Satisfactory	 Marginal	 Poor	 Cracked glass

Evidence of leaking insulated glass	 Broken/Missing hardware

| General Comments | See additional comments |
| --- | --- |

| Interior Windows / Glass |  |
| --- | --- |

Condition:	 Satisfactory	 Marginal	 Poor               Needs repair

Representative number of windows operated	 Painted shut   (See remarks)

Glazing compound needed     	 Cracked glass      Hardware missing     	 Broken counter-balance mechanism

Evidence of Leaking Insulated Glass:	 Yes	 No	 N/A 	Safety Glazing Needed: 	 Yes	 No

Security Bars Present:	 Yes	 No	 Not tested	 Safety hazard	 Test release mechanism before moving in

| Fireplace | None Location(s): |
| --- | --- |

Type:	 Gas 	 Wood	 Woodburner stove            Electric	 Ventless (See remarks)

Material:   Masonry	 Metal (pre-fabricated)	 Metal insert

Miscellaneous:	 Blower built-in    	Operable: 	 Yes	 No	Damper operable:	 Yes	 No

Open joints or cracks in firebrick/panels should be sealed	 Fireplace doors need repair

Damper Modified for Gas Operation:	 Yes	 No	 Damper missing

Hearth Extension Adequate:	 Yes	 No	Mantel: 	 N/A	 Secure 	 Loose

Physical Condition:	 Satisfactory	 Marginal	 Poor	 Recommend having flue cleaned and re-examined

| Stairs / Steps / Balconies |  |
| --- | --- |

Satisfactory	 Marginal	 Poor 	 None

Handrail:		 Satisfactory	 Marginal	 Poor	 Safety hazard

Hand Rail/Railing/Balusters Recommended

Risers/Treads:		 Satisfactory	 Marginal	 Poor	 Risers/Treads uneven

| Smoke / Carbon Monoxide Detectors | (See remarks) |
| --- | --- |

Present:		 Smoke Detector: 	 Yes	 No		Operable: 	 Yes	 No	 Not tested

CO Detector: 	 Yes	 No		Operable: 	 Yes	 No	 Not tested

| Attic/STRUCTURE/FRAMING/INSULATION | N/A (See remarks) |
| --- | --- |

Access: 	 Stairs	 Pulldown	 Scuttlehole/Hatch	 No access

Inspected From: 	 Access panel	 In the attic

Location: 	 Bedroom hall	 Bedroom closet	 Garage

Access Limited By: ____________________________________________________________________________________

Flooring: 	 Complete	 Partial	 None

Insulation: 	 Fiber glass	 Batts	 Loose	 Cellulose    Foam

Vermiculite	 Rockwoll	      Depth:              Recommend Baffles @ Eaves

Damaged	 Displaced		 Missing	 Compressed

Installed In: 	 Rafters      Walls	 Between ceiling joists	 Underside of  Roof Deck      Not visible

Recommend additional insulation (See comments)

Vapor Barriers:	 Kraft/foil faced	 Plastic	 Not visible	 Improperly Installed

Ventilation:	 Ventilation appears adequate	 Recommend additional ventilation

Fans Exhausted To:	Attic:    Yes	 No	Outside:   Yes	 No	 Not visible

HVAC Duct:  N/A Satisfactory Damaged Split Disconnected Leaking Repair/Replace  Recommend Insulation

Chimney Chase: 	 N/A 	 Satisfactory	 Needs repair	 Not visible

Structural Problems Observed:	 Yes	 No	 Recommend repair	 Recommend Structural Engineer

Roof Structure: 	 Rafters	 Trusses	 Wood	 Metal

Collar Ties	 Purlins	 Knee Wall	 Not Visible

Ceiling Joists: 	 Wood	 Metal	 Not visible

Sheathing: 	 Plywood	 OSB	 Planking	 Rotted	 Stained	 Delaminated

Evidence of Condensation/Moisture Leaking:	 Yes	 No	(See remarks)

Firewall Between Units: 	 N/A 	 Yes	 No 	 Needs repair/sealing

Electrical:	 Open junction box(es)	 Handyman wiring	 Visible knob-and-tube

| General Comments |  |
| --- | --- |

| Stairs |  |
| --- | --- |

Condition:	 Satisfactory	 Marginal	 Poor 	 Typical wear and tear	 Need repair

Handrail:	 Yes	 No	Condition:   	 Satisfactory		 Loose

Handrail/Railing/Balusters Recommended

Headway Over Stairs:	 Satisfactory	 Low clearance	 Safety hazard

| Foundation |  |
| --- | --- |

Condition:	 Satisfactory	 Marginal	 Have evaluated	 Monitor

Material:            ICF	 Brick 	 Concrete block	 Fieldstone	 Poured concrete

Horizontal Cracks:	 North	 South	 East	 West

Step Cracks:	 North	 South	 East	 West

Vertical Cracks:	 North	 South	 East	 West

Covered Walls:	 North	 South	 East		 West

Movement Apparent:	 North	 South	 East	 West

Indication Of Moisture:	 Yes	 No	 Fresh 	 Old stains

| Basement Walls |  | North |  |
| --- | --- | --- | --- |
| Diagram indicates where wall not visible |  |  |  |  |  |
| and type of covering: |  |  |  |  |  |
| P = Paneling | C = Crack(s) |  |  |  |  |  |
| D = Drywall | M = Monitor | West |  |  |  | East |
| S = Storage | E = Evaluate |  |  |  |  |  |
| O = Other |  |  | South |  |  |

Condition reported above reflects visible portion only

| Floor |  |
| --- | --- |

Material: 	 Concrete	 Dirt/Gravel	 Not visible 	 
Condition:	 Satisfactory	 Marginal	 Poor 	 Typical cracks

| Seismic Bolts |  |
| --- | --- |

N/A	 None visible	 Appear satisfactory	 Recommend evaluation

| Drainage |  |
| --- | --- |

Sump Pump:	 Yes	 No	 Working	 Not working 	 Needs cleaning 	 Pump not tested

Floor Drains:	 Yes	 Not visible	 Drains not tested

| Girders / Beams |  |
| --- | --- |

Material: 	 Steel  	 Wood  	 Concrete	 Block	 LVL  	 Not visible
Condition:	 Satisfactory  	 Marginal  	 Poor  	 Stained/rusted

| Columns |  |
| --- | --- |

Material: 	 Steel  	 Wood  	 Concrete	 Block	 Not visible
Condition:	 Satisfactory  	 Marginal  	 Poor  	 Stained/rusted

| Joists |  |
| --- | --- |

Material: 	 Wood  	 Steel  	 Truss  	 Not visible

2x8	 2x10	 2x12 	 Engineered I-Type	 Sagging/altered joists

Condition:	 Satisfactory  	 Marginal  	 Poor

| Sub Floor |  |
| --- | --- |

Indication of moisture stains/rotting

** Areas around shower stalls, etc., as viewed from basement or crawl space

| General Comments |  |
| --- | --- |

| Crawl Space | N/A Full crawlspace Combination basement/crawl space/slab |
| --- | --- |

Conditioned (heated/cooled): 	 Yes	 No

| Access | Exterior Interior hatch/door Via basement No Access |
| --- | --- |

Inspected from:	 Access panel	 In the crawl space

| Foundation Walls |  |
| --- | --- |

Material:	 Satisfactory	 Marginal	 Have evaluated	 Monitor

Concrete block	 Poured Concrete	 Stone	 IFC

Wood	 Brick	 Piers & columns

Cracks	 Movement

| Floor | Concrete Gravel Dirt |
| --- | --- |

Typical cracks	 Not Visible

| Seismic Bolts |  |
| --- | --- |

N/A	 None visible	 Appear satisfactory	 Recommend evaluation

| Drainage | Sump pump: Yes No Operable: Yes No Pump Not tested |
| --- | --- |

Standing Water:	 Yes	 No	 Not visible	Evidence of moisture damage:  Yes	 No

| Ventilation | Wall vents Power vents None apparent |
| --- | --- |

| Girders / Beams / Columns | Steel Wood Masonry Not visible |
| --- | --- |

Condition:	 Satisfactory  	 Marginal  	 Poor

| Joists | Material: Wood Steel Truss Not visible |
| --- | --- |

2x8	 2x10	 2x12 	 Engineered I-Type	 Sagging/altered joists

Condition:	 Satisfactory  	 Marginal  	 Poor

| Sub Floor | indication of moisture stains/rotting |
| --- | --- |

**Areas around shower stalls, etc., as viewed from basement or crawl space.

| Insulation | None Type: |
| --- | --- |

Location: 	 Walls	 Between floor joists

| Vapor Barrier |  |
| --- | --- |

Yes	 No					
 Kraft/foil face	 Plastic	 Not visible

| Crawlspace Walls |  | North |  |
| --- | --- | --- | --- |
| Diagram indicates where wall not visible |  |  |  |  |  |
| and type of covering: |  |  |  |  |  |
| P = Paneling | C = Crack(s) |  |  |  |  |  |
| D = Drywall | M = Monitor | West |  |  |  | East |
| S = Storage | E = Evaluate |  |  |  |  |  |
| O = Other |  |  | South |  |  |
| General Comments |  |

| Water Service | Main Shut-off Location: |
| --- | --- |

Water Entry Piping:	 Not visible	 Copper/Galv.	 Plastic* (PVC, CPVC, Polybutylene, PEX)	 Lead

Lead Other Than Solder Joints:	 Yes	 No	 Unknown 	 Service entry

Visible Water Distribution Piping:	 Copper	 Galvanized	 Plastic* (PVC, CPVC, Polybutylene, PEX)

Condition:	 Satisfactory	 Marginal	 Poor

Functional Flow:	 Satisfactory	 Marginal	 Poor		 Water pressure over 80 psi

Pipes, Supply/Drain:	 Corroded	 Leaking	 Valves broken/missing

Dissimilar metal	Cross connection: 	 Yes 	 No

Drain/Waste/Vent Pipe:	 Copper	 Cast iron	 Galvanized 	 PVC	 ABS

Condition:	 Satisfactory	 Marginal	 Poor

Support/Insulation:	 N/A	Type:

Traps Proper P-Type:	 Yes	 No	 P-traps recommended

Functional Drainage:	 Satisfactory	 Marginal	 Poor

Interior Fuel Storage System:	 N/A	 Yes       No	Leaking:  	 Yes 	 No

Gas Line:	 N/A 	 Copper	 Brass	 Black iron 	 Stainless steel	 CSST	 Not visible

Condition:	 Satisfactory	 Marginal	 Poor		 Recommend plumber evaluate

| Main Fuel Shut-Off Location | N/A |
| --- | --- |

| Well Pump | N/A Submersible In basement Well house Well pit Shared well |
| --- | --- |

Pressure Gauge Operable:	 Yes	 No	Well pressure:  ??? psi		 Not visible

| Sanitary / Grinder Pump | N/A Sealed Crock: Yes No |
| --- | --- |

Check Valve:	 Yes 	 No	Vented:	 Yes 	 No	Operable: 	           Yes 	 No

| Water Heater #1 | N/A |
| --- | --- |

Brand name: 		Serial #: ???

Type:	 Gas	 Electric	 Oil

Capacity: 	 gal.	Approx. age:   year(s)	Combustion Air Venting Present:	 Yes	 No	 N/A

Seismic restraints needed:	 Yes 	 No	 N/A

Relief Valve:	 Yes	 No	Extension proper:	 Yes 	 No	 Missing	 Recommend repair

Vent Pipe:	 N/A	 Satisfactory	 Pitch proper	 Improper	 Rusted	 Recommend repair 
Condition:	 Satisfactory	 Marginal	 Poor

| Water Heater #2 | N/A |
| --- | --- |

Brand name: 		Serial #: ???

Type:	 Gas	 Electric	 Oil

Capacity: 	 gal.	Approx. age:   year(s)	Combustion Air Venting Present:	 Yes	 No	 N/A

Seismic restraints needed:	 Yes 	 No	 N/A

Relief Valve:	 Yes	 No	Extension proper:	 Yes 	 No	 Missing	 Recommend repair

Vent Pipe:	 N/A	 Satisfactory	 Pitch proper	 Improper	 Rusted	 Recommend repair 
Condition:	 Satisfactory	 Marginal	 Poor

| Water Softener | (Unit not evaluated) Loop Installed: Yes No |
| --- | --- |

Plumbing Hooked Up:	 Yes 	 No	Softener Present:	 Yes	 No	Plumbing Leaking:	 Yes 	 No

| General Comments |  |
| --- | --- |

| Heating System - Unit #1 | Location: (See remarks) |
| --- | --- |

#1 Brand Name: 		Approximate age:  year(s)	 Unknown

Model #: ???	Serial #: ???

#2 Brand Name: 		Approximate age:  year(s)	 Unknown

Model #: ???	Serial #: ???

Energy Source:	 Gas	 LP	 Oil 	 Electric	 Solid Fuel

Warm Air System:	 Belt drive	 Direct drive	 Gravity	 Central system	 Floor/Wall unit

Heat Exchanger:	 N/A (sealed)	 Visual w/mirror	 Flame distortion	 Rusted	 Carbon/soot buildup

Carbon Monoxide:	 N/A	 Detected at Plenum/Register	 Not tested

CO Test:	Tester: 	Combustion Air Venting Present:	 N/A   Yes	 No

Controls:	Disconnect:   Yes	 No	 Normal operating and safety controls observed

Distribution:	 Metal duct   Insulated flex duct    Cold air returns	 Duct board	 Asbestos-like wrap

Flue Piping:	 N/A               Satisfactory                Rusted	              Improper slope	 Safety hazard

Filter:	 Standard	 Electrostatic	 Satisfactory	 Needs cleaning/replacement	 Missing

When Turned On By Thermostat:	 Fired	 Did not fire 	Proper Operation: 	 Yes	 No	 Not tested

Heat Pump:	 N/A     Aux. electric  Aux. gas  Sub-Slab ducts: Water/Sand Observed:  N/A  Yes   No

#1 – System Condition:	 Satisfactory	 Marginal	 Poor	 Recommended HVAC Technician Examine

#2 – System Condition:	 Satisfactory	 Marginal	 Poor	 Recommended HVAC Technician Examine

System Not Operated Due To: 	 Exterior temperature

| Boiler System | N/A |
| --- | --- |

Brand Name: 		Approximate age:  year(s)	 Unknown

Model #: ???	Serial #: ???

Energy Source:	 Gas	 LP	 Oil	 Electric	 Solid Fuel

Distribution:	 Hot water	 Baseboard	 Steam 	 Radiator	 Radiant Floor

Circulator:	 Pump	 Gravity	 Multiple zones

Controls:	Temp/pressure gauge exist:	 Yes	 No	Operable:	 Yes	 No

Oil Fired Units:	Disconnect:	 Yes	 No	Combustion Air Venting Present:	 Yes	 No	 N/A

Relief valve:	 Yes	 No	 Missing	Extension proper:	 Yes	 No

Operated:	When turned on by thermostat:	 Fired	 Did not fire

Operation:	Satisfactory:	 Yes	 No	 Recommend HVAC technician examine	 Before closing

| Other Systems | N/A Electric baseboard Radiant ceiling cable |
| --- | --- |

Gas space heater	 Woodburning stove	(See Remarks)

Proper Operation:	 Yes	 No

System Condition:	 Satisfactory	 Marginal	 Poor

| General Comments |  |
| --- | --- |

| Main Panel | Location: Condition: Satisfactory Marginal Poor |
| --- | --- |

Adequate Clearance To Panel: 	 Yes	 No	Amperage:  Volts 120/240	 Breakers	 Fuses

Appears Grounded:	 Yes	 No	 Not visible

GFCI Breaker: 	 Yes	 No	Operable: 	 Yes	 No

AFCI Breaker: 	 Yes	 No	Operable: 	 Yes	 No

Main Wire:	 Copper	 Aluminum	 Not visible	 Double tapping of the main wire

Condition:	 Satisfactory	 Poor 	 Federal Pacific Panel Stab Lok®  (See remarks)*

Branch Wire:	 Copper	 Aluminum*	 Not visible

Condition:	 Satisfactory	 Poor 	 Recommend electrician evaluate/repair*

Romex	 BX cable	 Conduit 	 Knob & tube**

Double tapping	 Wires undersized/oversized breaker/fuse

Panel not accessible	 Not evaluated   Reason:

| Sub Panel(s) | None apparent |
| --- | --- |

Location 1: 	Location 2: 	Location 3:

Panel not accessible	 Not evaluated   Reason:

Branch Wire:	 Copper	 Aluminum

Neutral/ground separated: 	 Yes	 No 	Neutral isolated: 	 Yes	 No	 Safety hazard

Condition:	 Satisfactory	 Marginal	 Poor	 Recommend separating/isolating neutrals

| Electrical Fixtures | A representative number of installed lighting fixtures, switches, and receptacles |
| --- | --- |

located inside the house, garage, and exterior walls were tested and found to be:

Condition:	 Satisfactory	 Marginal	 Poor 	 Open grounds	 Reverse polarity

GFCIs not operating	 Solid conductor aluminum branch wiring circuits*

Ungrounded 3-prong receptacles 	(See remarks)

Recommend electrician evaluate/repair*

| Unit | Central system Wall Unit Location: Age: yrs. |
| --- | --- |

Energy Source:	 Electric	 Gas

Unit Type:	 Air cooled	 Water cooled	 Geothermal	 Heat pump

Evaporator Coil:	 Satisfactory	 Not visible	 Needs cleaning	 Damaged

Refrigerant lines:	 Leak	 Damage	 Insulation missing		 Satisfactory

Condensate Line/Drain:	 To exterior	 To pump	 Floor drain

Operation:	Differential ??? (F

Difference in temperature (split) should be 14-22( Fahrenheit	(See remarks)

Condition:	 Satisfactory	 Marginal	 Poor 	 Recommend HVAC technician examine/clean/service

Not operated due to exterior temperature

| Unit | Central system Wall Unit Location: Age: yrs. |
| --- | --- |

Energy Source:	 Electric	 Gas

Unit Type:	 Air cooled	 Water cooled	 Geothermal	 Heat pump

Evaporator Coil:	 Satisfactory	 Not visible	 Needs cleaning	 Damaged

Refrigerant lines:	 Leak	 Damage	 Insulation missing		 Satisfactory

Condensate Line/Drain:	 To exterior	 To pump	 Floor drain

Operation:	Differential ??? (F

Difference in temperature (split) should be 14-22( Fahrenheit	(See remarks)

Condition:	 Satisfactory	 Marginal	 Poor 	 Recommend HVAC technician examine/clean/service

Not operated due to exterior temperature

| General Comments |  |
| --- | --- |

ITEMS NOT OPERATING

MAJOR CONCERNS

Item(s) that have failed or have potential of failing soon.

POTENTIAL SAFETY HAZARDS

DEFERRED COST ITEMS

Items that have reached or are reaching their normal life expectancy or show indications that they may require repair or replacement anytime during the next five (5) years.

*	Items listed in this report may inadvertently have been left off the Summary Sheet.  Customer should read the entire report, including the Remarks.

SERVICE WALKS/DRIVEWAYS

Spalling concrete cannot be patched with concrete because the new will not bond with the old. Water will freeze between the two layers, or the concrete will break up from movement or wear. Replacement of the damaged section is recommended. Walks or driveways that are close to the property should be properly pitched away to direct water away from the foundation. Asphalt driveways should be kept sealed and larger cracks filled so as to prevent damage from frost.

PATIOS

that have settled towards the structure should be mudjacked or replaced to assure proper pitch. Improperly

pitched patios are one source of wet basements/crawlspaces.

EXTERIOR WOOD SURFACES

All surfaces of untreated wood need regular applications of paint or special chemicals to resist damage. Porch or deck columns and fence posts which are buried in the ground and made of untreated wood will become damaged within a year or two.

Decks should always be nailed with galvanized, stainless steal or aluminum nails. Decks that are not painted or stained should be treated with a water sealer.

GRADING AND DRAINAGE

Any system of grading or landscaping that creates positive drainage (moving water away from the foundation walls) will help to keep a basement and crawlspace dry. Where negative grade exists and additional backfill is suggested, it may require digging out around the property to get a proper pitch. Dirt shall be approximately 6” below the bottom sill and should not touch wood surfaces.

Flower beds, loose mulched areas, railroad ties and other such landscaping items close to the foundation trap moisture and contribute to wet basements. To establish a positive grade, a proper slope away from the house is 1” per foot for approximately 5-6 feet. Recommend ground cover planting or grass up to foundation.

ROOF AND SURFACE WATER CONTROL

Roof and surface water must be controlled to maintain a dry basement and crawlspace. This means keeping gutters cleaned out and aligned, extending downspouts, installing splashblocks, and building up the grade so that roof and surface water is diverted away from the building.

WINDOW WELLS

The amount of water which enters a window well from falling rain is generally slight, but water will accumulate in window wells if the yard is improperly graded. Plastic window well covers are useful in keeping out leaves and debris.

RETAINING WALLS

Retaining walls deteriorate because of excessive pressure buildup behind them, generally due to water accumulation. Conditions can often be improved by excavating a trench behind the retaining wall and filling it with coarse gravel. Drain holes through the wall will then be able to relieve the water pressure.

Retaining walls sometime suffer from tree root pressure or from general movement of topsoil down the slope. Normally, these conditions require rebuilding the retaining wall.

RAILINGS

It is recommended that railings be installed for any stairway over 3 steps and porches over 30” for safety reasons. Balusters for porches, balconies, and stairs should be close enough to assure children cannot squeeze through.

DEFINITIONS

SATISFACTORY (Sat.) - Indicates the component is functionally consistent with its original purpose but may show signs of normal wear and tear and deterioration.

MARGINAL (Marg.) - Indicates the component will probably require repair or replacement anytime within five years.

POOR - Indicates the component will need repair or replacement now or in the very near future.

Valleys and Flashings that are covered with shingles and/or tar or any other material are considered not visible and

are not part of the inspection.

Tar and Gravel Roofs  - This type of covering on a pitched roof requires ongoing annual maintenance. We

recommend that a roofing contractor evaluate this type of roof. Infra-red photography is best used to determine

areas of potential leaks.

Flat roofs are very vulnerable to leaking. It is very important to maintain proper drainage to prevent the ponding of

water. We recommend that a roofing contractor evaluate this type of roof.

| ROOF TYPE | LIFE EXPECTANCY | SPECIAL REMARKS |
| --- | --- | --- |
| Asphalt Shingles | 15-20 years | Used on nearly 80% of all residential roofs; requires little maintenance. |
| Asphalt Multi-Thickness Shingles* | 20-30 years | Heavier and more durable than regular asphalt shingles. |
| Asphalt Interlocking. Shingles* | 15-25 years | Especially good in high-wind areas. |
| Asphalt Rolls | 10 years | Used on low slope roofs. |
| Built-up Roofing | 10-20 years | Used on low slope roofs; 2 to 3 times as costly as asphalt shingles. |
| Wood Shingles* | 10-40 years1 | Treat with preservative every 5 years to prevent decay. |
| Clay Tiles*, Cement Tiles* | 20 + years 20 + years | Durable, fireproof, but not watertight, * requiring a good subsurface base. |
| Slate Shingles* | 30-100 years 2 | Extremely durable, but brittle and expensive. |
| Asbestos Cement Shingles* | 30-75 years | Durable, but brittle and difficult to repair. |
| Metal Roofing | 15-40 + years | Comes in sheets & shingles; should be well grounded for protection from lightning; certain metals must be painted. |
| Single Ply | 15-25 years | New material; not yet passed test of time. |
| Membrane (mfgr’s claim) Polyurethane with Elastomenic Coating | 5-10 years 1 | Used on low slope roofs. |

* Not recommended for use on low slope roof

1 Depending on local conditions and proper installation

2 Depending on quality of slate

Roof coverings should be visually checked in the spring and fall for any visible missing shingles, damaged coverings or other defects. Before re-roofing, the underside of the roof structure and roof sheathing should be inspected to determine that the roof structure can support the additional weight of the shingles.

Wood shakes and shingles will vary in aging, due to the quality of the material, installation, maintenance, and surrounding shade trees. Ventilation and drying of the wood material is critical in extending the life expectancy of the wood. Commercial preservatives are available on the market, which could be applied to wood to impede deterioration.

CHIMNEYS

Chimneys built of masonry will eventually need tuckpointing. A cracked chimney top that allows water and carbonic acid to get behind the surface brick/stone will accelerate the deterioration. Moisture will also deteriorate the clay flue liner. Periodic chimney cleaning will keep you apprised of the chimney’s condition. The flashing around the chimney may need resealing and should be inspected every year or two. Fireplace chimneys should be inspected and evaluated by a chimney professional before using. Chimneys must be adequate height for proper drafting. Spark arrestors are recommended for a wood burning chimney, and chimney caps for fossil fuels. Unlined Chimney - should be re-evaluated by a chimney technician. Have flue cleaned and re-evaluated. The flue lining is covered with soot or creosote and no representation can be made as to the condition.

NOT EVALUATED

The flue was not evaluated due to inaccessibility such as roof pitch, cap, cleanout not accessible, etc.

CRICKET FLASHING

Small, sloped structure made of metal and designed to drain moisture away from a chimney. Usually placed at the back of a chimney.

GUTTERS AND DOWNSPOUTS

This is an extremely important element in basement/crawlspace dampness control. Keep gutters clean and downspout extensions in place (4’ or more). Paint the inside of galvanized gutters, which will extend the life. Shortly after a rain or thaw in winter, look for leaks at seams in the gutters. These can be recaulked before they cause damage to fascia or soffit boards. If no gutters exist, it is recommended that they be added.

SIDING

Wood siding should not come in contact with the ground. The moisture will cause rotting to take place and can attract carpenter ants. See page 34 for siding that have known problems, but are not always recognizable. Brick and stone veneer must be monitored for loose or missing mortar. Some brick and stone are susceptible to spalling. This can be caused when moisture is trapped and a freeze/thaw situation occurs. There are products on the market that can be used to seal out the moisture. This holds true for brick and stone chimneys also. Metal siding will dent and scratch. Oxidation is a normal reaction in aluminum. There are good cleaners on the market and it is recommended that they be used occasionally. Metal siding can be painted.

EIFS This type of siding is a synthetic stucco and has experienced serious problems. It requires a certified EIFS inspector to determine condition.

DOORS AND WINDOWS

These can waste an enormous amount of energy. Maintain the caulking around the frames on the exterior. Check for drafts in the winter and improve the worst offenders first. Windows that have leaky storm windows will usually have a lot of sweating. Likewise, well-sealed storms that sweat indicate a leaky window. It is the tighter unit that will sweat (unless the home has excess humidity to begin with).

Wood that exhibits blistering or peeling paint should be examined for possible moisture sources: roof leaks, bad

gutters, interior moisture from baths or laundry or from a poorly vented crawl space. Some paint problems have no

logical explanation, but many are a symptom of an underlying problem. A freshly painted house may mask these

symptoms, but after you have lived in the home for a year or two, look for localized paint blistering (peeling). It may

be a clue.

New glazing will last longer if the raw wood is treated with boiled linseed oil prior to glazing. It prevents the wood

from drawing the moisture out of the new glazing.

CAULKING

Many different types of caulk are available on the market today. Check with a paint or hardware store for the kind of application you need.

OVERHEAD DOOR OPENERS

We recommend that a separate electrical outlet be provided. Openers that do not have a safety reverse are considered a safety hazard. Small children and pets are especially vulnerable. We recommend the operating switches be set high enough so children cannot reach them. If a electric sensor is present, it should be tested occasionally to ensure it is working.

GARAGE SILL PLATES should be elevated or treated lumber should be used. If this is not the case, try to direct water away to prevent rotting.

BURNERS

Any appliance such as a water heater, furnace, etc. should have the flame a minimum of 18" above the floor. Any open flame less

PLASTER ON WOOD LATH

Plaster on wood lath is an old technique and is no longer in general use. Wood lath shrinks with time and the nails rust and loosen. As a result, the plaster may become fragile and caution is needed in working with this type of plastering system. Sagging ceilings are best repaired by laminating drywall over the existing plaster and screwing it to the ceiling joists.

PLASTER ON GYPSUM LATH (ROCK LATH)

Plaster on gypsum lath will sometimes show the seams of the 16” wide gypsum lath, but this does not indicate a structural fault. The scalloping appearance can be leveled with drywall joint compound and fiberglass mesh joint tape or drywall can be laminated over the existing plaster on the ceiling.

WOOD FLOORING

Always attempt to clean wood floors first before making the decision to refinish the floor. Wax removers and other mild stripping agents plus a good waxing and buffing will usually produce satisfactory results. Mild bleaching agents help remove deep stains. Sanding removes some of the wood in the floor and can usually be done safely only once or twice in the life of the floor.

NAIL POPS

Drywall nail pops are due to normal expansion and contraction of the wood members to which the drywall is nailed and are usually of no structural significance.

CARPETING

Where carpeting has been installed, the materials and condition of the floor underneath cannot be determined.

APPLIANCES (If report indicated appliances were operated, the following applies) Dishwashers are tested to see if the motor operates and water sprays properly. Stoves are tested to see that burners are working and oven and broiler get hot. Timer and controls are not tested. Refrigerators are not tested. Most new Dishwashers have the drain line looped automatically and may not be visible on the day of inspection. It is essential for the dishwasher drain line to have an anti-siphon break to prevent backflow. A drain line loop or Dishwasher air gap should be installed if found to be missing. No representation is made to continued life expectancy of any appliance.

ASBESTOS AND OTHER HAZARDS

Asbestos fibers in some form are present in many homes, but are often not visible and cannot be identified without testing.

If there is reason to suspect that asbestos may be present and if it is of particular concern, a sample of the material in question may be removed and analyzed in a laboratory. However, detecting or inspecting for the presence or absence of asbestos is not a part of our inspection.

Also excluded from this inspection and report are the possible presence of, or danger from, radon gas, lead-based paint, urea formaldehyde, toxic or flammable chemicals and all other similar or potentially harmful substances and environmental hazards.

WINDOWS

A representative number of windows are inspected.

STALL SHOWER

The metal shower pan in a stall shower has a potential or probable life of 10-20 years depending on quality of the pan installed. Although a visible inspection is made to determine whether a shower pan is currently leaking, it cannot be stated with certainty that no defect is present or that one may not soon develop. Shower pan leaks often do not show except when the shower is in actual use.

CERAMIC TILE

Bathroom tile installed in a mortar bed is excellent. It is still necessary to keep the joint between the tile and the tub/shower caulked or sealed to prevent water spillage from leaking through and damaging the ceilings below.

Ceramic tile is often installed in mastic. It is important to keep the tile caulked or water will seep behind the tile and cause deterioration in the wallboard. Special attention should be paid to the area around faucets and other tile penetrations.

EXHAUST FANS

Bathrooms with a shower should have exhaust fans when possible. This helps to remove excess moisture from the room, preventing damage to the ceiling and walls and wood finishes. The exhaust fan should not be vented into the attic. The proper way to vent the fan(s) is to the outside. Running the vent pipe horizontally and venting into a gable end or soffit is preferred. Running the vent pipe vertically through the roof may cause condensation to run down the vent pipe, rusting the fan and damaging the wallboard. Insulating the vent pipe in the attic will help to reduce this problem.

SLOW DRAINS on sinks, tubs, and showers are usually due to build up of hair and soap scum. Most sink popups can be easily removed for cleaning. Some tubs have a spring attached to the closing lever that acts as a catch for hair. It may require removing a couple of screws to disassemble. If you cannot mechanically remove the obstruction, be kind to your pipes. Don’t use a caustic cleaner. There are several bacteria drain cleaners available. They are available at hardware stores in areas where septic tanks are used. These drain cleaners take a little longer to work, but are safe for you and your pipes.

SAFETY HAZARDS

Typical safety hazards found in bathrooms are open grounds or reverse polarity by water. Replacing these outlets with G.F.C.I.’s are recommended. (See page 28)

WHIRLPOOL TUBS

This relates to interior tubs hooked up to interior plumbing. Where possible, the motor will be operated to see that the jets are working. Hot tubs and spas are not inspected.

DOOR STOPS

All swinging doors should be checked for door stops. Broken or missing door stops can result in door knobs

breaking through drywall or plaster.

CLOSET GUIDES

Sliding closet doors should be checked to see that closet guides are in place. Missing or broken closet guides can

cause scratches and damage to doors.

COLD AIR RETURNS

Bedrooms that do not have cold air returns in them should have a 3/4” gap under the doors to allow cold air to be

drawn into the hall return.

AN INSPECTION VERSUS A WARRANTY A home inspection is just what the name indicates, an inspection of a home...usually a home that is being purchased. The purpose of the inspection is to determine the condition of the various systems and structures of the home. While an inspection performed by a competent inspection company will determine the condition of the major components of the home, no inspection will pick up every minute latent defect. The inspector’s ability to find all defects is limited by access to various parts of the property, lack of information about the property and many other factors. A good inspector will do his or her level best to determine the condition of the home and to report it accurately. The report that is issued is an opinion as to the condition of the home. This opinion is arrived at by the best technical methods available to the home inspection industry. It is still only an opinion. A warranty is a policy sold to the buyer that warrants that specific items in the home are in sound condition and will remain in sound condition for a specified period of time. Typically, the warranty company never inspects the home. The warranty company uses actuarial tables to determine the expected life of the warranted items and charges the customer a fee for the warranty that will hopefully cover any projected loss and make a profit for the warranty seller. It is essentially an insurance policy. The service that we have provided you is an inspection. We make no warranty of this property. If you desire warranty coverage, please see your real estate agent for details about any warranty plan to which their firm may have access.

WINDOW FRAMES AND SILLS

Window frames and sills are often found to have surface deterioration due to condensation that has run off the window and damaged the varnish. Usually this can be repaired with a solvent style refinisher and fine steel wool. This is sometimes a sign of excess humidity in the house. See comments regarding caulking doors and windows, page 8.

FIREPLACES

It is important that a fireplace be cleaned on a routine basis to prevent the buildup of creosote in the flue, which can cause a chimney fire. Masonry fireplace chimneys are normally required to have a terra cotta flue liner or 8 inches of masonry surrounding each flue in order to be considered safe and to conform with most building codes. During visual inspections, it is not uncommon to be unable to detect the absence of a flue liner either because of stoppage at the firebox, a defective damper or lack of access from the roof.

WOODBURNERS

Once installed, it can be difficult to determine proper clearances for woodburning stoves. Manufacturer specifications, which are not usually available to the inspector, determine the proper installation. We recommend you ask the owner for paperwork, verifying that it was installed by a professional contractor.

VENTILATION

Ventilation is recommended at the rate of one square foot of vent area to 300 square feet of attic floor space, this being divided between soffit and rooftop. Power vents should ideally have both a humidistat and a thermostat, since ventilation is needed to remove winter moisture as well as summer heat. Evidence of condensation such as blackened roof sheathing, frost on nail heads, etc. is an indication that ventilation may have been or is blocked or inadequate.

INSULATION

The recommended insulation in the attic area is R-38, approximately 12”. If insulation is added, it is important that the ventilation is proper.

SMOKE DETECTORS

Smoke detectors should be tested monthly. At least one detector should be on each level. CO detectors are not required by most states, but for safety reasons, are highly recommended.

VAPOR BARRIERS

The vapor barrier should be on the warm side of the surface. Most older homes were built without vapor barriers. If the vapor barrier is towards the cold side of the surface, it should be sliced or removed. Most vapor barriers in the attic are covered by insulation and therefore, not visible.

SAFETY GLAZING

Safety glazing requirements vary depending on the age of the home. Every attempt is made to identify areas where the lack of safety glazing presents an immediate safety hazard, such as a shower door. In some older homes it is difficult to determine if safety glazing is present, since the glass is not marked. Therefore, no representation is made that safety glazing exists in all appropriate areas.

INSULATED GLASS

Broken seal in thermopane/insulated windows are not always visible nor detectible due to humidity and temperature changes during the day. Other factors such as window covering, dirty windows, and lack of accessibility, personal property placed in front of the windows all affect the view of the windows at the time of the inspection.

BASEMENT/CRAWLSPACE

Any basement/crawlspace that has cracks or leaks is technically considered to have failed. Most block basements/crawlspace have step cracks in various areas. If little or no movement has occurred and the step cracks are uniform, this is considered acceptable. Horizontal cracks in the third or fourth block down indicate the block has moved due to outside pressure. They can be attributed to many factors such as improper grading, improperly functioning gutter and downspout system, etc. Normally if little or no movement has taken place and proper grading and downspouts exist, this is considered acceptable. If the wall containing the stress crack(s) has moved considerably, this will require some method of reinforcement. Basements/crawlspace that have been freshly painted or tuckpointed should be monitored for movement. This will be indicated by cracks reopening. If cracks reappear, reinforcement may be necessary. Reinforcing a basement/crawlspace wall can become expensive.

FOUNDATION (COVERED WALLS)

Although an effort has been made to note any major inflections or weaknesses, it is difficult at best to detect these areas when walls are finished off, or basement/crawlspace storage makes areas inaccessible. No representation is made as to the condition of these walls.

INSULATED CONCRETE FORMS (ICF’S) are formwork for concrete that stays in place as permanent building insulation for energy-efficient, cast-in-place, reinforced concrete walls, floors and roofs.

MONITOR indicates that the walls have stress cracks, but little movement has occurred. In our opinion, the cracks should be filled with mortar and the walls monitored for further movement and cracking. If additional movement or cracking occurs, reinforcement may be necessary.

HAVE EVALUATED We recommend that the walls be re-evaluated by a structural engineer or basement/crawlspace repair company and estimates be obtained if work is required.

VAPOR BARRIER

Floors that are dirt or gravel should be covered with a vapor barrier.

MOISTURE PRESENT

Basement/crawlspace dampness is frequently noted in houses and in most cases the stains, moisture or efflorescence present is a symptom denoting that a problem exists outside the home. Usual causes are improper downspout extensions or leaking gutters and/or low or improper grade (including concrete surfaces) at the perimeter of the house. A proper slope away from the house is one inch per foot for four to six feet. Expensive solutions to basement/crawlspace dampness are frequently offered. It is possible to spend thousands of dollars on solutions such as pumping out water that has already entered or pumping of chemical preparations into the ground around the house, when all that may be necessary are a few common sense solutions at the exterior perimeter. However, this is not intended to be an exhaustive list of causes and solutions to the presence of moisture.

No repre-sentation is made to future moisture that may appear.

PALMER VALVE

Many older homes have a valve in the floor drain. This drain needs to remain operational.

DRAIN TILE

We offer no opinion about the existence or condition of the drain tile, as it cannot be visibly inspected.

BASEMENT ELECTRICAL OUTLETS

We recommend that you have an outlet within 6' of each appliance. The appliance you plan to install may be different than what exists, therefore the inspection includes testing a representative number of receptacles that exist. It is also recommended to have ground fault circuit interrupts for any outlet in the unfinished part of the basement and crawl spaces.

CRAWL SPACES

Crawl spaces are shallow spaces between the first level floor joist and the ground. Access to this area may be from the inside, outside or not accessible at all. Ductwork, plumbing, and electrical may be installed in the space in which access may be necessary. The floor of the crawl space may be covered with concrete, gravel, or may be the original soil. A vapor barrier may be a sheet of plastic or tar paper and installed over or under this material. The vapor barrier will deter the moisture from the earth from escaping into the crawl space and causing a musty smell. Ventilation is also important to control excess moisture buildup. Vents may be located on the outside of the house and are normally kept open in the summer and closed for the winter (where freezing may occur). The basement/crawl space diagram indicates areas that are covered and not part of a visual inspection. Every attempt is made to determine if paneling is warped, moisture stains are bleeding through, etc. Storage that blocks the visibility of a wall is not removed to examine that area. Therefore, it is important that on your walk-through before closing, you closely examine these areas. Closed crawl spaces that have vents to the outside should have insulation under the floor above the crawl space.

HAVE EVALUATED

We recommend that the walls be re-evaluated by a structural engineer or basement repair company and estimates be obtained if work is required.

MONITOR

Indicates that the walls have stress cracks, but little movement has occurred. In our opinion, the cracks should be filled with mortar and the walls monitored for further movement and cracking. If additional movement or cracking occurs, reinforcement may be necessary.

FOUNDATION (COVERED WALLS)

Although an effort has been made to note any major inflections or weaknesses, it is difficult at best to detect these areas when walls are finished off, or basement/crawlspace storage makes areas inaccessible. No representation is made as to the condition of these walls.

MOISTURE PRESENT

Basement/crawlspace dampness is frequently noted in houses and in most cases the stains, moisture or efflorescence present is a symptom denoting that a problem exists outside the home. Usual causes are improper downspout extensions or leaking gutters and/or low or improper grade (including concrete surfaces) at the perimeter of the house. A proper slope away from the house is one inch per foot for four to six feet. Expensive solutions to basement/crawlspace dampness are frequently offered. It is possible to spend thousands of dollars on solutions such as pumping out water that has already entered or pumping of chemical preparations into the ground around the house, when all that may be necessary are a few common sense solutions at the exterior perimeter. However, this is not intended to be an exhaustive list of causes and solutions to the presence of moisture.

No repre-sentation is made to future moisture that may appear.

WELLS

Examination of wells is not included in this visual inspection. It is recommended that you have well water checked for purity by the local health authorities and, if possible, a check on the flow of the well in periods of drought. A well pit should have a locked cover on it to prevent anyone from falling into the pit.

SEPTIC SYSTEMS

The check of septic systems is not included in our visual inspection. You should have the local health authorities or other qualified experts check the condition of the septic system. In order for the septic system to be checked, the house must have been occupied within the last 30 days.

WATER PIPES

Galvanized water pipes rust from the inside out and may have to be replaced within 20 to 30 years. This is usually done in two stages: horizontal piping in the basement first, and vertical pipes throughout the house later as needed. Copper pipes usually have more life expectancy and may last as long as 60 years before needing to be replaced.

HOSE BIBS

During the winter months it is necessary to make sure the outside faucets are winterized. This can be done by means of a valve located in the basement. Leave the outside faucets open to allow any water standing in the pipes to drain, preventing them from freezing. Hose bibs cannot be tested when winterized.

WATER HEATER

The life expectancy of a water heater is 5-10 years. Water heaters generally need not be replaced unless they leak. It is a good maintenance practice to drain 5-10 gallons from the heater several times a year. Missing relief valves or improper extension present a safety hazard.

WATER SOFTENERS

During a visual inspection it is not possible to determine if water is being properly softened.

PLUMBING

The temperature/pressure valve should be tested several times a year by lifting the valve’s handle. Caution: very hot water will be discharged. If no water comes out, the valve is defective and must be replaced.

SHUT-OFF VALVES

Most shut-off valves have not been operated for long periods of time. We recommend operating each shut-off valve to: toilet bowl, water heater, under sinks, main shut-off, hose faucets, and all others. We recommend you have a plumber do this, as some of the valves may need to be repacked or replaced. Once the valves are in proper operating order, we recommend opening and closing these valves several times a year.

POLYBUTYLENE PIPING

This type of piping has a history of problems and should be examined by a licensed plumber and repaired or replaced as necessary.

MECHANICAL DEVICES MAY OPERATE AT ONE MOMENT AND LATER MALFUNCTION; THEREFORE, LIABILITY IS SPECIFICALLY LIMITED TO THOSE SITUATIONS WHERE IT CAN BE CONCLUSIVELY SHOWN THAT THE MECHANICAL DEVICE INSPECTED WAS INOPERABLE OR IN THE IMMEDIATE NEED OF REPAIR OR NOT PERFORMING THE FUNCTION FOR WHICH IS IT WAS INTENDED AT THE TIME OF INSPECTION.

CSST

Corrugated Stainless Steel Tubing is an alternative to traditional black iron gas piping. It is a continuous, flexible, stainless steel pipe with an exterior PVC covering.

HEATING AND AIR CONDITIONING units have limited lives. Normal lives are:

GAS-FIRED HOT AIR . . . . . . . . . . . . . . . .15-25 years

OIL-FIRED HOT AIR . . . . . . . . . . . . . . . . .20-30 years

CAST IRON BOILER . . . . . . . . . . . . . . . . .30-50 years

(Hot water or steam) or more

STEEL BOILER . . . . . . . . . . . . . . . . . . . . .30-40 years

(Hot water or steam) or more

COPPER BOILER . . . . . . . . . . . . . . . . . . . .10-20 years

(Hot water or steam)

CIRCULATING PUMP (Hot water) . . . . . .10-15 years

AIR CONDITIONING COMPRESSOR . . . .8-12 years

HEAT PUMP . . . . . . . . . . . . . . . . . . . . . . . ..8-12 years

Gas-fired hot air units that are close to or beyond their normal lives have the potential of becoming a source of carbon monoxide in the home. You may want to have such a unit checked every year or so to assure yourself that it is still intact. Of course a unit of such an age is a good candidate for replacement with one of the new, high efficiency furnaces. The fuel savings alone can be very attractive.

Boilers and their systems may require annual attention. If you are not familiar with your system, have a heating contractor come out in the fall to show you how to do the necessary thing Caution: do not add water to a hot boiler!

Forced air systems should have filters changed every 30 to 60 days of the heating and cooling season. This is especially true if you have central air conditioning. A dirty air system can lead to premature failure of your compressor - a $1,500 machine.

Oil-fired furnaces and boilers should be serviced by a professional each year. Most experts agree you will pay for the service cost in fuel saved by having a properly tuned burner.

Read the instructions for maintaining the humidifier on your furnace. A malfunctioning humidifier can rust out a furnace rather quickly. It is recommended that the humidifier be serviced at the same time as the furnace, and be cleaned regularly. During a visual inspection it is not possible to determine if the humidifier is working.

Have HVAC technician examine - A condition was found that suggests a heating contractor should do a further analysis. We suggest doing this before closing.

Heat exchangers cannot be examined nor their condition determined without being disassembled. Since this is not possible during a visual, non-technically exhaustive inspection, you may want to obtain a service contract on the unit or contact a furnace technician regarding a more thorough examination.

Testing pilot safety switch requires blowing out the pilot light. Checking safety limit controls requires disconnecting blower motor or using other means beyond the scope of this inspection. If the furnace has not been serviced in last 12 months you may want to have a furnace technician examine.

CO Test - This is not part of a non-technical inspection. If a test was performed, the type of tester is indicated on page 27.

Combustible Gas Detector - If a gas detector was used during the inspection of the furnace and evidence of possible combustible gases was noted, we caution you that our test instrument is sensitive to many gases and not a foolproof test. None-the-less, this presents the possibility that a hazard exists and could indicate that the heat exchanger is, or will soon be, defective.

Every effort has been made to evaluate the size of the service. Three wires going into the home indicate 240 volts. The total amperage can be difficult to determine. We highly recommend that ground fault circuit interrupters (G.F.C.I.) be connected to all outlets around water. This device automatically shuts the circuit off when it senses a current leak to ground. This device can be purchased in most hardware stores. G.F.C.I.’s are recommended by all outlets located near water, outside outlets, or garage outlets. Pool outlets should also be protected with a G.F.C.I.

See diagram below:

If you do have G.F.C.I.’s, it is recommended that you test (and reset) them monthly. When you push the test button, the reset button should pop out, shutting off the circuit. If it doesn’t, the breaker is not working properly. If you don’t test them once a month, the breakers have a tendency to stick and may not protect you when eeded.

Knob and tube wiring found in older homes should be checked by an electrician to insure that the wire cover is in good condition. Under no circumstances should this wire be covered with insulation. Recess light fixtures should have a baffle around them so that they are not covered with insulation. The newer recessed fixtures will shut off if they overheat. (no representation is made as to proper recess lighting fixtures).

Federal Pacific Stab-Lok® Electrical panels may be unsafe.  See

www.google.com (Federal Pacific)

Aluminum wiring in general lighting circuits has a history of over heating, with the potential of a fire. If this type of wiring exists, a licensed electrical contractor should examine the whole system.

ARC FAULTS

In some areas arc Faults are required for bedrooms in new homes starting in 2002. In some areas arc Faults are required for all 120 Volt circuits that are not GFCI protected in new homes starting in 2009. Updrade as desired forenhanced safely.

REVERSE POLARITY

A common problem that surfaces in many homes is reverse polarity. This is a potentially hazardous situation in which the hot and neutral wires of a circuit are reversed at the outlet, thereby allowing the appliance to incorrectly be connected. This is an inexpensive item to correct.

Each receptacle has a brass and silver screw. The black wire should be wired to the brass screw and the white wire should go to the silver screw. When these wires are switched, this is called “reverse polarity.” Turning off the power and switching these wires will correct the problem.

Main service wiring for housing is typically 240 volts. The minimum capacity for newer homes is 100 amps though many older homes still have 60 amp service. Larger homes or all electric homes will likely have a 200 amp service.

Main service wiring may be protected by one or more circuit breakers or fuses. While most areas allow up to six main turnoffs, expanding from these panels is generally not allowed.

COOLING

Testing A/C System and Heat Pump- The circuit breakers to A/C should be on for a minimum of 24 hours and the outside temperature at least 60 degrees for the past 24 hours or an A/C system cannot be operated without possible damage to the compressor. Check the instructions in your A/C manual or on the outside compressor before starting up in the summer. Heat pump can only be tested in the mode it’s running in. Outside temperature should be at least 65° for the past 24 hours to run in cooling mode.

Temperature differential, between 14°-22°, is usually acceptable. If out of this range, have an HVAC contractor examine it. It is not always feasible to do a differential test due to high humidity, low outside temperature, etc.

A/C CONDENSER COIL They should not become overgrown with foliage. Clearance requirements vary, but 2’ on all sides should be considered minimal with up to 6’ of air discharge desirable. If a clothes dryer vent is within five to ten feet, either relocate the vent or do not run when the A/C is running. The lint will quickly reduce the efficiency of the A/C unit.

COSTS OF REMODELING OR REPAIR

The prices quoted below include a range of prices based on a typical metropolitan area. Individual prices from contractors can vary substantially from these ranges. We advise that several bids be obtained on any work exceeding several hundred dollars. DO NOT RELY ON THESE PRICES... GET FURTHER ESTIMATES.

ITEM 	UNIT	ESTIMATED PRICE

Masonry fireplace 			Each 			$3,000 - $6,000

Install prefab fireplace			Each 			2,000 - 4,000

Insulate attic 				Square foot 		.75 - 1.25

Install attic ventilating fan 			Each 			200 - 300

Install new drywall over plaster 		Square foot 		1.75 - 2.75

Install new warm air furnace 		Each 			2,000 - 3,000

Replace central air conditioning 		Each 			1,400 - 2,000

Install humidifier 			Each 			300 - 500

Install electrostatic air cleaner		Each 			800 - 1,500

Increase elec. svc. to 60-100 amps 		Each 			600 - 1,200

Run separate elec. line for dryer 		Each 			125 - 200

Run separate elec. line for A/C 		Each 			135 - 200

Install hardwired smoke detector 		Each 			100 - 180

Install new disposal 			Each 			250 - 400

Install new dishwasher 			Each 			500 - 750

Install new hot water boiler 		Each 			2,000 - 4,000

Install new 30-40 gal water heater 		Each 			350 - 650

Install new 30 gal. water heater 		Each 			300 - 500

Dig and install new well 			Each 			get estimate

Install new septic system 			Each 			get estimate

Regrade around exterior 			Each 			500 - 900

Install new sump pump and pit 		Each 			400 - 600

Build new redwood or pressure- 		Square foot 		20 - 30

treated deck

Install storm windows 			Each 			60 - 150

Install wood replacement windows 		Each 			400 - 800

Install aluminum or vinyl 			Each 			300 - 800

replacement window

Install new gutters and downspouts 		Linear foot 		3.50 - 5.00

Install asphalt shingle o/existing 		Square foot 		1.20 - 1.70

Tear off existing roof and install 		Square foot 		2.50 - 4.00

new asphalt shingle roof

Instl 1-ply membrane rubberized roof 	Square foot 		get estimate

Instl new 4-ply built-up tar & gravel 	Square foot 		get estimate

Remove asbestos from pipes in bsmt 	Linear foot 		get estimate

Concrete drive or patio 			Square foot 		3.00 - 4.00

with removal of old 			Square foot 		2.25 - 3.00

Clean chimney flue 			Each 			100 - 200

Add flue liner for gas fuel 						900 - 1,200

Add flue liner for oil or wood 					2,800 - 3,500

Deferred Costs - It is impossible to determine how long these items will last before needing replacement. The report

addresses most of these items from a “condition” standpoint.

PREVENTIVE MAINTENANCE TIPS

I. FOUNDATION and MASONRY: Basements, Exterior Walls: To prevent seepage and

condensation problems.

a. Check basement for dampness and leakage after wet weather.

b. Check chimneys, deteriorated chimney caps, loose and missing mortar.

c. Maintain grading sloped away from foundation walls.

II. ROOFS, GUTTERS, and EAVESTROUGH: To prevent roof leaks, condensation, seepage, and

decay problems.

a. Check for damaged, loose or missing shingles, blisters.

b. Clean gutters, leaders, strainers, window wells, drains. Be sure downspouts direct water away from

foundation. Cut back tree limbs.

c. Check flashings around roof stacks, vents, skylights, chimneys, as sources of leakage. Check vents,

louvers and chimneys for birds nests, squirrels, insects.

d. Check fascias and soffits for paint flaking, leakage and decay.

III. EXTERIOR WALLS: To prevent paint failure, decay, and moisture penetration problems.

a. Check painted surface for paint flaking or paint failure. Cut back shrubs.

b. Check exterior masonry walls for cracks, looseness, missing or broken mortar.

IV. DOORS AND WINDOWS: To prevent air and weather penetration problems.

a. Check caulking for decay around doors, windows, corner boards, joints. Recaulk and weatherstrip as

needed. Check glazing, putty around windows.

V. ELECTRICAL: For safe electrical performance, mark and label each circuit.

a. Trip circuit breakers every six months and ground fault circuit interrupters (G.F.C.I.) monthly.

b. Check condition of lamp cords, extension cords and plugs. Replace at first sign of wear and damage.

c. Check exposed wiring and cable for wear or damage.

d. If you experience slight tingling shock from handling or touching any appliance, disconnect the

appliance and have it repaired. If lights flicker or dim, or if appliances go on and off unnecessarily, call a

licensed electrician.

VI. PLUMBING: For preventive maintenance.

a. Drain exterior water lines, hose bibbs, sprinklers, pool equipment in the fall.

b. Draw off sediment in water heaters monthly or per manufacturer’s instructions.

c. Have septic tank cleaned every 2 years.

VII. HEATING and COOLING: For comfort, efficiency, energy conservation and safety.

a. Change or clean furnace filters, air condition filters, electronic filters as needed.

b. Clean and service humidifier. Check periodically and annually.

c. Have oil burning equipment serviced annually.

VIII. INTERIOR: General house maintenance.

a. Check bathroom tile joints, tub grouting and caulking. Be sure all tile joints in bathrooms are kept well

sealed with tile grout to prevent damage to walls, floors and ceilings below.

b. Close crawl vents in winter and open in summer.

c. Check underside of roof for water stains, leaks, dampness & condensation, particularly in attics and

around chimneys.

IX. Know the location of:

• Main water shutoff valve.

• Main emergency shutoff switch for the heating system.

• Main electrical disconnect or breaker.